## Slide 1: JNCIA-Junos
Ben Jacobson
Network Engineer
LinkedIn:
Covering JN0-103 Exam Topics
Your photo
https://www.linkedin.com/in/benjamin-jacobson-bb318143/

## Slide 2: Junos OS Fundamentals
Juniper software architecture and traffic handling

## Slide 3: Junos OS Architecture
Overview of Junos OS and FreeBSD Kernel
#

## Slide 4: Unix-based FreeBSD
Same source code base on all platforms
The same base code is used in all Juniper hardware, though some may have additional features that run as separate processes. This allows for maintenance and set up tasks to remain largely similar
Process daemons
Daemon is the name for a service or process that runs in the background. As JNCIA we’re expected to be aware of a few of the common daemons, their names and their function
Function are split into separate software processes Separate processes allows for segregation of tasks. This shields each process from one another through separate
memory and execution space. A problem with one process is unlikely to affect other processes.

## Slide 5: Common Daemons
rpd
  Routing Protocol Daemon runs within the Routing Engine. Functions include routing table updates, implementation of routing policies, and handling of routing messages
mgd
  The management daemon serves as the broker between the external entities interacting with the device and the internal processes. It manages the setup of the device when in configuration mode, and the collecting of information from other processes when in operational mode
dcd
  Device control daemon is responsible for configuring interfaces based on current configuration and available hardware

## Slide 6
INSR ICON