## Slide 1: Junos OS Fundamentals
Juniper software architecture and traffic handling

## Slide 2: Control / Forwarding Planes
The Routing Engine and Packet Forwarding Engine
#

## Slide 3: Control and Forwarding Planes
Control Plane
  The control plane is made up of the Routing Engine (RE) which is responsible for rpd, handling chassis components, system management, user access, etc. Importantly, the RE manages the Routing Table (RT), and from it derives the Forwarding Table (FT)
Forwarding Plane
  The forwarding plane is made up of the Packet Forwarding Engine (PFE). The PFE uses the FT to forward transit traffic through the device. Any traffic which does not match to the FT or requires further processing will be forwarded to the RE
Control Plane
Forwarding Plane
RT
FT
FT
Routing Engine
Packet Forwarding Engine

## Slide 4: Routing Engine
Junos OS
  The Routing Engine runs Junos OS
  and consists of all processes and PCI
  platform which the OS runs on
6 main functions
  Handling of routing protocol packets
  Management interface
  Configuration management
  Accounting and alarms
  Modular Software
  Scalability
Notes: PCI - Peripheral Component Interconnect

## Slide 5: Packet Forwarding Engine
Transit traffic
  The PFE’s primary job is to handle and forward
  transit traffic to the correct destination, as quickly
  as possible
3 components with ASICs
  Switching control board
  Physical Interface Card (PIC)
  Flexible PIC Concentrator (FPC)
Notes: PCI - Peripheral Component Interconnect

## Slide 6: Additional Resources
https://www.juniper.net/documentation/en_US/junos/topics/concept/junos-software-architecture.html
Notes: PCI - Peripheral Component Interconnect