## Slide 1: Junos OS Configuration
Setting up a Juniper device

## Slide 2: Initial Configuration
Identifying factory defaults and setting initial configuration
#

## Slide 3: Factory Default Configuration
Amnesiac
  Factory default configuration sets the device’s hostname to amnesiac and can be a quick method of determining the factory defaults have been loaded.
No root password
  The factory default password for the root user account is to have no password. Junos forces the administrator to change this before any other configurations may be committed

## Slide 4: Hostname, NTP, Root PW
Root user password
  This is a required configuration item by Junos. No other configuration changes can be committed until the password has been set.
Hostname
  Setting a hostname on your device is not only good to identify its purpose or location, but also a quick method to confirm the configuration has been edited.
NTP server
  Having accurate time on your device is important for function and troubleshooting. Certificates can cease to work correctly if the clock is too far off from other devices; and without accurate time it’s difficult to troubleshoot with logs
Notes: Note all of these items are in the system hierarchy

## Slide 5: SNMP and Syslogging
SNMP community and client list
  Simple Network Management Protocol has been a management tool of choice for a long time due to its simplicity to implement and wide range of tools supporting it.
Syslog server
  Sending syslogs to an external collector is best practice. It will help when troubleshooting issues later and having a record of changes to the system.
Notes: Example steps
Load factory defaults, point out amnesiac and no root password
Try committing a change without setting root password, show it’s denied.

## Slide 6: Local User Accounts
Local username and password
  Local user authentication can be configured with multiple users with varying privilege levels. A password must be set for the user in order for the account to log into the device.
Notes: Show factory default device with no root password and amnesiac hostname
Set root password, hostname, and NTP server
Set SNMP community and client-list, set syslogging host
Create local username and password
Exit and show new hostname
Login with new account