## Slide 1: Junos OS Configuration
Setting up a Juniper device

## Slide 2: Juniper Device Interfaces
Interface types and naming schemes
#

## Slide 3: Interface Categories
2 Categories of interfaces
  Juniper devices have 2 broad categories of interfaces, Network and Special interfaces.
Network Interfaces
  Physically connect to the network and carry network traffic
Special Interfaces
  Can be virtual or physical and perform functions like routing, management or monitoring
5 types of interfaces
  Permanent
  Transient
  Network
  Services
  Container
Notes: Permanent interfaces—Interfaces that are always present in the router. Permanent interfaces in the router consist of management Ethernet interfaces and internal Ethernet interfaces
Transient interfaces—Interfaces that can be inserted into or removed from the router depending on your network configuration needs.
Networking interfaces—Interfaces, such as Ethernet or SONET/SDH interfaces, that primarily provide traffic connectivity.
Services interfaces—Interfaces that provide specific capabilities for manipulating traffic before it is delivered to its destination.
Container interfaces—Interfaces that support automatic protection switching (APS) on physical SONET links using a virtual container infrastructure.

## Slide 4: Network Interfaces
Vary based on device hardware
  Interface types available will vary depending on the hardware. We’ll be listing the interfaces available on the EX series switches, a common series for the JNCIA to handle
Aggregated ethernet
LAN access
Power over Ethernet (PoE)
Trunks
Physical interface names use the following
format regardless of type and hardware:
interface-type-fpc/pic/port.unit
Examples:
ge-0/1/0.0
xe-1/0/0.250

## Slide 5: Special Interfaces
Can be physical or logical
  Some special interfaces, like the console port or virtual chassis ports, are physical interfaces used for management and switch interconnects. Other special interfaces, like loopback interfaces and Routed VLAN Interfaces (RVI) are logical and do not have a physical connection.
5 Types of Special Interfaces to be aware of
  Console port
  Loopback interface
  Dedicated Management Interface
  IRB / RVI (logical routed interface)
  Virtual Chassis Port
Notes: Example steps:
Log into device and show interfaces terse
Show unit number on an interface in configuration and output
Show chassis hardware, show numbering

## Slide 6: Additional Resources
https://www.juniper.net/documentation/en_US/junos/topics/concept/interfaces-interface-naming-overview.html
https://www.juniper.net/documentation/en_US/junos/topics/topic-map/switches-interface-understanding.html