## Slide 1: Routing Fundamentals
How a Juniper device makes forwarding decisions

## Slide 2: Tables and Instances
Separation of routing information
#

## Slide 3: Routing Tables - Unicast
Separation by type
  Juniper devices use separate routing tables based on the type and format of information that is stored. For instance MPLS LSP information is different from IPv4 Unicast which is different from IPv6 Unicast.
Protocols make updates to a table
  Dynamic routing protocols can interact with many different routing tables. OSPFv3 carries IPv6 unicast information. MP-BGP can carry information for multiple protocols, like MPLS LSP and IPv4 Unicast.
Table | Description
inet.0 | For IP version 4 (IPv4) unicast routes. This table stores interface local and direct routes, static routes, and dynamically learned routes.
inet.2 | This table stores unicast routes that are used for multicast reverse-path-forwarding (RPF) lookup in a specific format needed for DVMRP.
inet6.0 | For IP version 6 (IPv6) unicast routes. This table stores interface local and direct routes, static routes, and dynamically learned routes.
Notes: inet.2—For subsequent address family indicator (SAFI) 2 routes, when multiprotocol BGP (MBGP) is enabled. This table stores unicast routes that are used for multicast reverse-path-forwarding (RPF) lookup. The routes in this table can be used by the Distance Vector Multicast Routing Protocol (DVMRP), which requires a specific RPF table. In contrast, Protocol Independent Multicast (PIM) does not need this table because it can perform RPF checks against the inet.0 table. You can import routes from inet.0 into inet.2 using routing information base (RIB) groups, or install routes directly into inet.2 from a multicast routing protocol.

## Slide 4: Routing Tables - Multicast
Updated by clients
  Clients send join messages which allows switches and routers to learn where multicast messages should be forwarded
Updated by dynamic protocols
  PIM and DVMRP are 2 multicast routing protocols that interact with inet.1 or inet6.1 and import/export routes into/out of the tables.
Table | Description
inet.1 | For IPv4 multicast forwarding cache.
inet6.1 | For IPv6 multicast forwarding cache.
Notes: Table stores the IPv6/IPv4 (S,G) group entries that are dynamically created as a result of join state information.

## Slide 5: Routing Instances
Creates a new set of routing tables
  For L3 VPN instances, a set of appropriate routing tables will be created for the routing instance. This allows for secure separation of routing information. Routing instances will not interact with each other by default
Must be referenced specifically
  Tables within an instance are referenced using the routing-instance-name.table-name syntax
Type | Description
vrf | VPN routing and forwarding (VRF) instance. Provides support for Layer 3 VPNs, where interface routes for each instance go into the corresponding forwarding table only. Required to create a Layer 3 VPN.
Virtual-router | This instance type is similar to a VPN routing and forwarding instance type, but used for non-VPN-related applications.
No-forwarding | This is the default routing instance. Do not create a corresponding forwarding instance. Use this routing instance type when a separation of routing table information is required. There is no corresponding forwarding table. All routes are installed into the default forwarding table.
l2vpn | Enable a Layer 2 VPN on the routing instance.
Notes: Example steps:
Show route, only inet.0
Set IPv4 and IPv6 IPs on interface
Commit and show addition of inet6.0
Create virtual-router instance and add interface
Show route, show both instances shown
Show only the instance routing table.

## Slide 6
INSR ICON