## Slide 1: Policies and Filters
Influencing routing and packet forwarding

## Slide 2: Routing Policies
An introduction to routing policies
#

## Slide 3: Purpose
Import vs. Export
  Routing policies modify routing information, either when a protocol inserts (imports) a route into the routing table, or when a protocol advertises (exports) a route from the routing table.
Many modifications available
  route metric
  load balancing policy
  tag
  color
  reject
  etc.
Notes: Note that only accept and reject actions are ‘terminating’

## Slide 4: Evaluation
Organized into terms
  Terms are named, and are evaluated from top to bottom, regardless of the name of the terms. Term names are only used for the network administrator to describe the term.
Evaluated until a terminating action is reached
  Accept, reject, and default action are the only terminating actions. Evaluation continues until one of these are reached.
Notes: Note the next term and next policy actions

## Slide 5: Example
Sets of from – then terms
  In a routing policy routes must be identified using a from clause, then some action is defined to apply to the route in a then clause. The identification process can be specifying a specific route prefix, a protocol, a tag or color, a route distinguisher and many other options.
From term not necessary
  If no from item is specified, the term would match all routes that are evaluated against it.
Must be applied to be evaluated
  Can be applied to a whole protocol or specific neighbors.
Notes: Show BGP learned 3.3.3.0/24
set policy-options policy-statement longer_24 term term1 then accept
set policy-options policy-statement longer_24 term term2 from route-filter 3.3.3.0/24 exact
set policy-options policy-statement longer_24 term term2 then reject
Apply import to BGP group
Commit and show effect
Move rejection term to above match-all term
Commit and show routes removed

## Slide 6
INSR ICON